## Slide 1: Automotive Vehicle Dynamics
Acceleration and Braking IV – Anti-Lock Braking
Sean Brennan
Department of Mechanical and Nuclear Engineering
Penn State University
sbrennan@psu.edu

## Slide 2: First, a few words about spelling, since this is a pet peeve for the instructor
Breaking - separating or causing to separate into pieces as a result of a blow, shock, or strain.
Braking - making a moving vehicle slow down or stop by using a brake

## Slide 3: Wheel slip control is critical for directional stability
If the slip reached 100% (locked wheels) a loss of stability can occur. Even if stability is maintained, the forces generated from a locked wheel aren’t the maximum forces  longer stopping distance.
Ideally we want to operate at the slip that gives the peak force
Fmax
Flocked
0
 peak
100%

## Slide 4: The difference in stopping distance is substantial

## Slide 5: Anti-Lock Braking Systems: Stopping Times From 160-0 MPH
ABS (t=4.9s)
No ABS (t=5.5s)
*Take note of the skid mark patterns

## Slide 6: ABS also ensures that the tires continue to rotate, providing directional stability

## Slide 7: How do we stay at the peak?
For braking: Assume there’s a maximum allowable brake torque : max
A simple control law to achieve peak slip is

## Slide 8: Pure on-off may be a bad idea
However, this requires lots of things that are impossible: 1. Knowledge of what  peak is exactly. 2. Infinitely fast brake torque response.
A more realistic response involves the generation of a brake pressure which then generates a brake torque. (steady state brake = Kb Pbrake.)

## Slide 9: The brakes cannot respond instantly
Let’s model the dynamics of the torque generation as a first order system.
where Cfill , Cdump are time constants of the fill and dump phases of the brake cylinder

## Slide 10: And we may want to limit cycling
The brake system also has a hold phase where
but we won’t use that now.
Let’s treat Pbrake as a constant supply pressure that’s regulated by an on-off solenoid valve.

## Slide 11: So how do we implement?
Kb is a function of brake radius, brake pad friction coefficient, brake temperature and number of pads.
Now we could try the same strategy as before:
But we’d still need to know exactly where peak was plus the solenoid valve would be constantly switching
Supply pressure

## Slide 12: Putting it all together, we obtain a simple ABS strategy
Better idea:
This is a simple example of ABS for braking.
cycling
min
max
100
Fx
this is the
result.

## Slide 13: Simple Example
Half-car model with 2 wheel degrees of freedom.
4 DOF system

## Slide 14: Simple Example
Braking Coefficient vs. Slip Curve

## Slide 15: Without ABS Wheel Slip Control
Vehicle Pos.
Pitch 
Front normal force (kN)

## Slide 16: With ABS Wheel Slip Control
Front normal force (kN)
cycling

## Slide 17: Student experiments (pulling ABS fuse to turn it off)
Initial Speed: 40 mph

## Slide 18: Distance depends on inflation pressure

## Slide 19
Case Study: Two vehicles were used to perform an experiment comparing ABS on vs off. Both vehicles have ABS, which can be disabled by removing a fuse.
Chrysler Concorde LXi
(Bright Platinum Metallic)
Mazda 3
(Black)

## Slide 20: The test was performed on a road with 100ft of measured track. Each vehicle ran at 40mph with ABS.
Chrysler Concorde LXI
56ft
Mazda 3
50ft

## Slide 21: NO ABS 40MPH
Chrysler Concorde LXI
68ft
Mazda 3
64ft

## Slide 22
40MPH w/ABS: 56ft
40MPH No ABS: 68ft
40MPH w/ABS: 50ft
40MPH No ABS: 64ft
Final results yielded a 17.6% and 21.9% increase in performance for the Concorde and Mazda 3, respectively with ABS enabled

## Slide 23: Traction control is like ABS, but for acceleration to prevent spin-out

## Slide 24: Traction control systems are very like ABS
Very similar strategies can be used to minimize wheel slip during acceleration.
In this case, use accel = Torque (1)  < min Torque (2)  > max accel (t – t) min <  < max
Torque (1) > Torque (2)

## Slide 25: Traction control is different than ABS in that we can use other inputs
These two torques are generated from a variety of sources.
Torque (1) is principally engine torque x gear ratio and is governed by the throttle angle.
Engine
Nonlinear
Dynamics
Throttle
angle

engine
Torque (1)

## Slide 26: What other methods?
Torque (2) is a reduced torque that is obtained by one of several ways 1. Reduced throttle angle 2. Spark timing 3. Application of brakes.
The conceptual idea is the same as with ABS.

## Slide 27: Hard problems in ABS and TCS?
What are some of the problems associated with ABS?
  How do we know the velocity of vehicle with respect to ground? (without a ground speed sensor)
  How do we determine road characteristics such as friction?

## Slide 28: Finally, let’s talk about some vehicle testing situations
What are the ethical issues of this test?