## Slide 1: Automotive Vehicle Dynamics
Driver-Vehicle Interaction
Sean Brennan
Modified from presentations from Andrew Alleyne, used with permission
All Rights Reserved

## Slide 2: So far we have examined the dynamics of the vehicle as a stand-alone system.
However, the driver is an important part of the overall system that will keep the vehicle following the proper direction on the road
….or not.

## Slide 3: The driver-vehicle system is actually a feedback loop with the driver providing the feedback using visual, inertial, haptic, and auditory cues
driver
steering
accelerator
& brakes
vehicle
Vehicle states:
Disturbances: wind/road
road
conditions
road path
speed, relative position, relative orientation

## Slide 4: One could argue that most of the behavior on the road is actually human-human interaction mediated by a vehicle
See “Development of a Driver Vehicle Module for the Interactive Highway Safety Design Model” Publication No. FHWA-HRT-08-019

## Slide 5: How do we model this feedback loop? We know that drivers respond to the road ahead of them mostly using visual cues…
lateral distance
preview distance

## Slide 6: We seek to isolate input/output relationships, so usually model one input to one output
road
conditions
road path
Driver inputs
steering
accelerator
& brakes
Driver outputs

## Slide 7: In this lecture, we consider only very simple models of the driver to be used in conjunction with our vehicle models
Accurate modeling of human behavior is an extremely difficult task.
But even analyzing gross behavior, we obtain some very good insights into how to drive better ourselves!

## Slide 8: For our modeling purposes, the driver consists of several individual components
eye
sensing
brain
processing and command generation
limbs and muscles
actuation
component:
function:

## Slide 9: There’s usually a (big) delay between sensing any signal and having it processed.
This includes perception delay (paying attention), plus the delay between developing a command (planning) and that command reaching the limbs (actuation)
Total delay is often referred to as the reaction time (0.1 sec to 2 seconds… or more)
time delay
time delay

## Slide 10: This pure-delay method generates the simplest driver feedback model
In simplest terms, the driver can be represented by a transfer function.
Kd is the driver gain and t is the lumped delay of the driver including sensor processing and command delay
Driver output
Driver input

## Slide 11: There’s also a limit to how fast you can move! (actuator dynamics)
Even after commands arrive at the limbs, there’s a delay before the actual task is performed by the muscle
In other words, there’s a maximum frequency signal that can be tracked by the limb!
  Dependent on limb size (i.e. inertia) & musculature
w
mag
Limbs have a bandwidth

## Slide 12: We can include the limb actuation dynamics into a driver feedback model
Define TD as the bandwidth for the neuromuscular dynamics.
Note that, , Kd and TD can (and will) change for different driving applications
  For example, distracted driving versus racing
Driver lag
Time delay

## Slide 13: The driver feedback depends on lateral or longitudinal positioning
The units for driver gain and driver lag are different for speed following (m/s) versus lane regulation (m) so Kd should be different for longitudinal vs. lateral tasks.
Similarly, the gain and the lag will be different between the arms/steering wheel actuation and foot/pedal actuation

## Slide 14: Problems with modeling: humans anticipate events (and have memory)
Often, humans are very good at anticipating events.
  Particularly if they’ve been in similar situations before.
    (It’s called learning and remembering)
The driver action can actually react a bit sooner than the events actually occur!
  In System Dynamics terms, humans can ‘add phase’ to the feedback system.

## Slide 15: One way to add phase is to use a simple lead controller model
Defining TL to be the driver ‘lead time,’
Question: What is y(s) and u(s)?
  y(s) is simpler; it’s the steer wheel angle or the throttle/brake pedal position.
  U(s) is harder; it’s often a combo of many things.
Driver output (steering)
Driver lead
Driver’s input (eyes)

## Slide 16: Why not just use PID control on position?
Let’s pretend we have a simple line-following idea… goal is to keep the vehicle along a prescribed path.
heading error
desired path
lateral error

## Slide 17: If use only lateral error, we cannot correct yaw angle errors
These three all have zero lateral error but only one is correct.
Remember, yaw motion is lightly damped…!

## Slide 18: It is difficult to control the vehicle using only c.g. lateral position information
For example, it is very hard to keep your car parallel to the center line while looking out the bottom of an open driver door.
What do they teach in high school Driver’s Ed?
  Look ahead of the vehicle and try to control this point.

## Slide 19: Preview: how a driver’s control is really done!
Vehicle longitudinal axis
Desired look-ahead point
error
Road path
From inside the vehicle:

## Slide 20: A view from above the vehicle shows that using preview is like using both yaw and lateral control
desired path
y
preview length = L
L*sin(y) = error from orientation mismatch
lateral error
total error

## Slide 21: For normal, “look-ahead” driving, we see that the driver acts like a state-feedback controller
lateral error + L*sin(y)
Gdriver(s)
Steer angle or steer angle command (if you include limb dynamics)
preview distance*heading angle error
L*y for small heading angle errors

## Slide 22: The look-ahead or preview distance is a critical factor
For pure lateral control (no preview), the input to the driver would be the lateral error.
The lateral error is given in Earth fixed coordinates for our purposes.
lateral error
Gdriver(s)
Steer angle or steer angle command (if you include limb dynamics)

## Slide 23: We need to reconcile body-fixed to earth-fixed tracking
In a general case, the earth fixed coordinates would have to move along with the road.
Xearth
Yearth

## Slide 24: There is such thing as too much look-ahead, or too little
The larger the look-ahead distance L is, the greater the relative contribution of yaw angle orientation to the driver feedback.
Yaw feedback has a tendency to stabilize the Driver-Vehicle system.
    It adds damping
More L=>more damped response which is beneficial…to a point.
  You can’t be looking a mile ahead to control the vehicle.

## Slide 25: The problem with developing models of humans… we don’t like to conform!
Risk homeostasis: proposed by Gerald J.S. Wilde to explain why crash rates do not seem to be declining with ABS
  The basic idea: if you make the vehicle safer to drive (by improving the human/vehicle system), humans will drive in more risky manner to compensate
  For example, if you have 4WD, you are more likely to drive in snow storms than if you didn’t!

## Slide 26: The other problem is that we don’t like vehicles making human-like decisions
This is called the “canny valley”
http://www.youtube.com/watch?v=1js5bD68Nw8&feature=player_embedded

## Slide 27: The canny valley gets deeper if things move… like vehicles
http://en.wikipedia.org/wiki/File:Mori_Uncanny_Valley.svg

## Slide 28: A key challenge with driving is that it is a giant psychology experiment
For example, are you more likely to get hurt by a car with a helmet or without when riding a bicycle near the road?

## Slide 29: Turns out: drivers give you less room if wearing a helmet!

## Slide 30: There’s a joke that, the more technology we develop to make cars safer, the more technology makes us behave unsafe
In 2011, Blackberry had an outage for 3 days. In Dubai and Abu Dhabi (strong Blackberry usage base then), accidents fell by 20 to 40 percent nationwide over those 3 days.

## Slide 31: ME 452 Automotive Vehicle Dynamics
Produced by the
College of Engineering, UIUC
© 2000 UIUC BOT,
Modifications by S. Brennan, PSU
© 2011 PSU
All Rights Reserved

## Slide 32: Confounding Factors
Amount of sleep
Doesn’t just affect driving.
    Obesity, Feb 2008 reports that sleep loss leads to excessive weight gain.
    If more than 2 hours a night missed, 92% more likely to be overweight.
Modified 2008/03

## Slide 33: Suggested Sleep?
Younger than 5 years: 11 hours
5 to 10 years: 10 hours
Older than 10 years: 9 hours
Modified 2008/03

## Slide 34: Driving Strategies
So, how should one drive in snow?